## Slide 1
Using REPowerEU at its full potential:
the role of hydrogen and direct electrification in displacing fossil gas demand
16/03/2022

## Slide 2: How to use renewable electricity to displace the most gas
Chart: 
| Heat Pumps replacing gas boilers in average German home | Using renewables directly in the grid replacing gas-fired electricity | Green hydrogen replacing grey hydrogen in industry | Green hydrogen replacing Natural gas for electricity production in power plants
 | 0.23 | 0.17 | 0.09375 | 0.0714
Green H2 for electricity production
Green H2 replacing grey H2
Renewables directly on the grid
Heat pumps to replace gas boilers*
Gas displaced in BCM per TWh of renewable electricity
*Based on German average household

## Slide 3: REPowerEU aims to nearly triple current renewable capacity in the next 8 years
All newly deployed Wind & PV combined in 2030 will be expected to produce a little over 1000 TWh of electricity per year.
That’s the equivalent of the current French and German demand combined.
Chart: Capacity (GW)
| Capacity (GW)
Current Solar | 139.4
Current Wind | 220
Additional Solar | 280.6
Additional Wind | 260
Addtional REpowerEU | 80

## Slide 4
Current RePowerEU
plans
Maximise gas phase-out, while kick-starting H2 market
Maximising gas
phase-out
Chart: 
| Replace Gas fired Electricity | Hydrogen Production
Amount of Energy (TWh) | 510 | 508.4902
Chart: 
| Gas fired Electricity | Heat Pumps
Amount of Energy (TWh) | 566 | 452.4902
Chart: 
| Gas fired Electricity | Hydrogen Production | Heat Pumps
Amount of Energy (TWh) | 566 | 133.152 | 319.3382
How will the EU choose to use its 1000TWh of renewable electricity?
Produced with RePowerEU additional capacity

## Slide 5: How will the EU choose to use its 1000TWh of renewable electricity?
Current REPowerEU plans
Maximise gas phase-out, while kick-starting H2 market
Chart: 
| Gas fired Electricity | Heat Pumps
Amount of Energy (TWh) | 566 | 452.4902
Chart: 
| Gas fired Electricity | Hydrogen Production | Heat Pumps
Amount of Energy (TWh) | 566 | 133.152 | 319.3382
Maximising gas phase-out
Chart: 
| Replace Gas fired Electricity | Hydrogen Production
Amount of Energy (TWh) | 510 | 508.4902
Produced with RePowerEU additional capacity

## Slide 6: REPowerEU = Still 24 BCM of Russian gas needed
Chart: 
| Replace Gas fired Electricity | Hydrogen Production
Amount of Energy (TWh) | 510 | 508.4902

## Slide 7: Maximising gas phase-out = No more RU gas + extra 43 BCM avoided
Chart: 
| Gas fired Electricity | Heat Pumps
Amount of Energy (TWh) | 566 | 452.4902

## Slide 8: Mixed approach = total RU gas phase-out + deployment of H2 economy
Chart: 
| Gas fired Electricity | Hydrogen Production | Heat Pumps
Amount of Energy (TWh) | 566 | 133.152 | 319.3382
Produced with RePowerEU additional capacity

## Slide 9
Using renewable electricity can reduce gas use substantially if used effectively.
Direct electrification offers the biggest reduction to gas: heat pumps are particularly effective at displacing gas demand.
Natural gas cannot be replaced en mass by hydrogen, given the large amount of renewables needed to displace small amounts of gas.
Relying on hydrogen will leave the EU with more fossil gas in the system.
A future-proof strategy needs to both drastically reduce our dependence on fossil fuels while also deploying hydrogen in no-regret sectors where other decarbonisation pathways don’t exist.
Additional electricity deployed for hydrogen production must be dimensioned on the hydrogen targets: RePowerEU foresees 80 GW of capacity for hydrogen production, only enough to produce 2.8 Mt of hydrogen per year, 20% of the proposed RED target.
Key Conclusions

## Slide 10
Get in touch!
marta@bellona.org
+32 (0) 489 638 862
Marta Lovisolo
Policy Advisor Renewable Energy Systems

## Slide 11
Thank You!

## Slide 12
EuroStat 2020 – Energy Statistics
Wind average utilisation – 27%
Solar average utilisation – 11%
80GW of additional RePower EU – 50% Wind, 50% solar
Gas Power (CCGT) efficiency – 60%
H2 electrolysis efficiency - 70%
Grey Hydrogen – 4.5 Nm3 of Natural Gas per kg of hydrogen
Heat Pumps – Assuming an average yearly heat pump consumption per household in Germany of 4993 kWh Schlemminger et al, 2022, Dataset on electrical single-family house and heat pump load profiles in Germany