## Slide 1: Pauline Nouallet, Senior Policy Analyst, ERCST Mehtap Alper, Senior Policy Researcher, ERCST
Public Event
EU Climate Policy and Electricity Market
Notes: It is a long slide show, so we’ll go quickly over background etc to have time to focus on the core issues!

## Slide 2
EU Climate Policy and Electricity Market
Introduction – Concept
Electricity Market Design Provisions on the vertical axis
  Short-term Pricing Mechanisms ;
  Medium to Long-term instruments;
  Flexibility Options;
Desirable Outcomes on the horizontal axis
  Short term operational signals
  Long term investment signals
  EU Competitive Advantage
  Affordability
  Security of Supply
Looking at how some of the Electricity Market Design Provisions, in interaction with EU-ETS and other climate policies, impact (positively or negatively) on the Desirable Outcomes.
Framework for analyzing the European Commission (EC) proposal on electricity market reform through the lens of Climate Change Policy - provide stakeholders with a tool and means for examining /analyzing the proposal through a climate change perspective
Matrix including the following:

## Slide 3
EU Climate Policy and Electricity Market
Framework matrix
Desirable Outcomes EMD Provisions | A. Short-term signals for decarbonization | B. Long-term signals for decarbonization | C. Competitiveness | D. Affordability | E. Security of Supply
1. Short-term Pricing Mechanisms |  |  |  |  | 
1. i) Marginal Pricing |  |  |  |  | 
Marginal Pricing Mechanism | + | o | o | o | +
1. ii) Market Interventions |  |  |  |  | 
Iberian Exception | - | - | + | + | o
Inframarginal Revenue Cap | - | - | + | + | o
Windfall Profit Tax | o | - | + | + | o
2. Medium to Long-term Instruments |  |  |  |  | 
PPAs, CFDs, Forward Markets | o | + | + | + | +
Capacity Remuneration Mechanisms | + | + | + | + | +
3. Flexibility Options |  |  |  |  | 
Flexibility Options (Storage and Demand Side Management) | + | + | + | + | +

## Slide 4
EU Climate Policy and Electricity Market
Framework matrix
Desirable Outcomes EMD Provisions | A. Short-term signals for decarbonization | B. Long-term signals for decarbonization | C. Competitiveness | D. Affordability | E. Security of Supply
1. Short-term Pricing Mechanisms |  |  |  |  | 
1. i) Marginal Pricing |  |  |  |  | 
Marginal Pricing Mechanism | + | o | o | o | +
1. ii) Market Interventions |  |  |  |  | 
Iberian Exception | - | - | + | + | o
Inframarginal Revenue Cap | - | - | + | + | o
Windfall Profit Tax | o | - | + | + | o
2. Medium to Long-term Instruments |  |  |  |  | 
PPAs, CFDs, Forward Markets | o | + | + | + | +
Capacity Remuneration Mechanisms | + | + | + | + | +
3. Flexibility Options |  |  |  |  | 
Flexibility Options (Storage and Demand Side Management) | + | + | + | + | +

## Slide 5
EU Climate Policy and Electricity Market
Framework matrix
Desirable Outcomes EMD Provisions | A. Short-term signals for decarbonization | B. Long-term signals for decarbonization
1. Short-term Pricing Mechanisms |  | 
1. i) Marginal Pricing |  | 
Marginal Pricing Mechanism and Merit Order | + | o
1. ii) Market Interventions |  | 
Iberian Exception | - | -
Inframarginal Revenue Cap | - | -

## Slide 6
EU Climate Policy and Electricity Market
Short-term pricing mechanisms and decarbonization signals
Interaction with Climate Policy (EU-ETS)
Phasing out fossil-fuel based electricity generation:
Plants are dispatched following the merit order principle (from lower to higher marginal production costs) until demand is met
The CO2 price is a component of these variable production costs for fossil fuel-based generation plants, those plants then incur higher marginal production costs
The CO2 price, embedded in these variable production costs, contribute to shifting these fossil-fuel based plants at the end of merit order and/or interchanging their dispatch contributing to fuel switching (depending on the level of the CO2 price and the level of the other price components, such as the price of fuel used)
Do they provide decarbonization signals?
Provide short-term signals for decarbonization:
The influence of the CO2 price on electricity price (CO2 price is passing through wholesale electricity price formation) incentivize:
  Producers to reduce the share of these variable costs attributed to carbon emissions, and
  Energy consumers to reduce their electricity bills: they are provided with clear signals, giving them the ability to adjust their consumption in line with changing conditions (increase energy efficiency as CO2 price increases)
Neutral impact on long-term signals for decarbonization:
  The functioning of the marginal pricing system in the EU and the way the contracts are framed in the wholesale market gives a short term signals for decarbonization and EU ETS complement each other in providing short-tem signals for decarbonisation but does not interfer / have a neutral impact on providing long-term signals for decarbonisation
Marginal Pricing and Merit Order

## Slide 7
Interaction with EU ETS
CO2 price signal may not be as effective at phasing out fossil fuel-based producers: the balance is different
Description of impacts on Desirable Outcomes
Does not provide short-term signals for decarbonization :
  Distortive effect on the marginal pricing system, which consequently does no longer provide short-term signals for decarbonization.
  This mechanisms subsidizes the purchase of natural gas: Generators producing electricity from gas-fired plants are compensated for the difference between the price cap and the market price; This consequently caps the electricity price in the wholesale market, limiting the rents of other producers and ensuring lower electricity prices for consumers.
  This mechanisms removes the price signals of gas for electricity generation and is therefore ineffective in reducing gas demand. It also removes to some extent the CO2 price signal associated to gaz.
  An increase in electricity production based on natural gas was observed, which can be indirectly linked to an increase of CO2 emissions in the short-term.
Does not provide long-term signals for decarbonization:
  Iberian model has succeeded in lowering electricity prices in Spain but, at the same time, does not provide any safeguards for long term contracts (such as PPAs). This mechanisms can potentially disadvantage consumers who have already hedged their risks through long-term contracts. It can also hamper consumer’s attractiveness for PPAs.
  Emergency interventions create policy uncertainty resulting in investments being postponed until a clearer and more stable market environment has been reached
EU Climate Policy and Electricity Market
Short-term pricing mechanisms and decarbonization signals
Market Interventions : The case of the Iberian mechanism

## Slide 8
Interaction with EU ETS
It determines the maximum amount of revenue a power plant can earn in the free electricity market according to its energy source.
The cap on market revenues are applied to technologies with low marginal production costs, such as for instance wind, solar, nuclear energy or lignite.
The price setting technologies i.e., coal and gas fired power plants are exempt from this intervention so, in theory, the marginal pricing mechanism and the EU ETS would still provide short-term signals for decarbonization (the merit order and the wholesale electricity price remain unchanged).
In practice, national implementations of the infra-marginal revenue caps differs and impact the competition between inframarginal technologies at the EU level (the level of this revenue cap differs between MS), and,at a national level (some MSs apply technology-specific price caps (i.e., Slovakia, France, Germany etc.), other MSs apply uniform level of price cap to all inframarginal technologies (i.e., Bulgaria)
Do they provide decarbonization signals?
Does not provide short-term signals for decarbonization :
  Although the application of the revenue caps to inframarginal generators should in theory not affect the merit order, this intervention can potentially be distortive depending on how it is designed. For instance, a revenue cap that applies only to the day ahead market or a very low-price cap may lead to a shift of inframarginal electricity production to other markets, such as intra-day market, balancing market or futures markets. This, therefore, leads to the less efficient dispatch of renewables in the spot market.
  Reducing gap between electricity prices during peak hours and off-peak hours weaken the signals for demand side flexibility. This may lead to increasing demand, which in turn may increase the production of carbon-based electricity during peak hours.
Does not provide short-term signals for decarbonization :
  Emergency interventions create policy uncertainty resulting in investments being postponed until a clearer and more stable market environment has been reached
  Reducing gap between electricity prices during peak hours and off-peak hours reduce the generators/producers’ opportunity for arbitrage (taking advantage of price differences). This may discourage variable generation facilities, such as wind or solar power plants, from investing in storage.
Market Interventions : Inframarginal Revenue Cap
EU Climate Policy and Electricity Market
Short-term pricing mechanisms and decarbonization signals

## Slide 9
EU Climate Policy and Electricity Market
Short-term pricing mechanisms and decarbonization signals
Overview
Desirable Outcomes EMD Provisions | A. Short-term signals for decarbonization | B. Long-term signals for decarbonization
1. Short-term Pricing Mechanisms |  | 
1. i) Marginal Pricing |  | 
Marginal Pricing Mechanism and Merit Order | + | o
1. ii) Market Interventions |  | 
Iberian Exception | - | -
Inframarginal Revenue Cap | - | -
The marginal pricing mechanism and the carbon market complement each other in the short-term in their role of providing decarbonization signals; They have a neutral impact on long-term signals for decarbonization as they do not interfere.
Markets interventions can have a distortive effect on the functioning of the marginal pricing mechanism and the CO2 price signal; Short-term/emergency interventions can also have negative long-term impacts: they create policy uncertainty resulting in investments being postponed until a clearer and more stable regulatory environment has been reached
Notes: In order to have long-term signals for decarbonisation, other longer-term measures need to be implemented. These measures would probably need to be framed on a period compatible With the return time on Investments to provide longer term price visibility or predictability